/*
 * Copyright (c) 2016, Freescale Semiconductor, Inc.
 * Copyright 2016-2017 NXP
 * All rights reserved.
 *
 * SPDX-License-Identifier: BSD-3-Clause
 */
#include "fsl_debug_console.h"
#include "board.h"
#include "fsl_sctimer.h"
#include "fsl_gpio.h"
#include "peripherals.h"
#include "pin_mux.h"
#include <stdbool.h>
/*****************************
 * Definitions
 *****************************
#define SCTIMER_CLK_FREQ CLOCK_GetFreq(kCLOCK_BusClk)
#define LEFT_MOTOR_SPEED1 kSCTIMER_Out_7
#define LEFT_MOTOR_DIRECTION1 kSCTIMER_Out_2
#define RIGHT_MOTOR_SPEED2 kSCTIMER_Out_4
#define RIGHT_MOTOR_DIRECTION2 kSCTIMER_Out_5
#define MOTOR_PORT 0U
#define left_motor_speed_PIN 18U
#define left_motor_dir_PIN 19U
#define right_motor_speed_PIN 20U
#define right_motor_dir_PIN 21U
/*****************************
 * Prototypes
 *****************************
/*****************************
 * Code
 *****************************
/*!
 * @brief Main function
 */
int main(void) {
uint32_t dutycycle_left=60,dutycycle_
/* Define the init structure for the output LED pin*/
   gpio_pin_config_t left_motor_speed = {
       kGPIO_DigitalInput, 1,
   };
   gpio_pin_config_t right_motor_speed = {
         kGPIO_DigitalInput, 1,
     };
   gpio_pin_config_t left_motor_dir = {
         kGPIO_DigitalInput, 1,
     };
   gpio_pin_config_t right_motor_dir = {
         kGPIO_DigitalInput, 1,
     };
sctimer_config_t sctimerInfo;
   sctimer_pwm_signal_param_t pwmParam_left1,pwmParam_left2,
   uint32_t event_left1,event_left2,event_
   uint32_t sctimerClock;
    /* Board pin, clock, debug console init */
    /* attach 12 MHz clock to FLEXCOMM0 (debug console) */
    CLOCK_AttachClk(BOARD_DEBUG_
    /* enable clock for GPIO*/
    CLOCK_EnableClock(kCLOCK_
    CLOCK_EnableClock(kCLOCK_
    BOARD_InitPins();
    BOARD_BootClockFROHF48M();
    BOARD_InitDebugConsole();
    GPIO_PortInit(GPIO, MOTOR_PORT);
    GPIO_PinInit(GPIO, MOTOR_PORT, left_motor_speed_PIN, &left_motor_speed);
    GPIO_PinInit(GPIO, MOTOR_PORT, right_motor_speed_PIN, &right_motor_speed);
    GPIO_PinInit(GPIO, MOTOR_PORT, left_motor_dir_PIN, &left_motor_dir);
    GPIO_PinInit(GPIO, MOTOR_PORT, right_motor_dir_PIN, &right_motor_dir);
    GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_speed_PIN);
    GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_dir_PIN);
    GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_speed_PIN);
    GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_dir_PIN);
    sctimerClock = SCTIMER_CLK_FREQ;
    /* Default configuration operates the counter in 32-bit mode */
    SCTIMER_GetDefaultConfig(&
    /* Initialize SCTimer module */
    SCTIMER_Init(SCT0, &sctimerInfo);
    /* Configure first PWM with frequency 24kHZ from LEFT MOTOR FIRST SIGNAL output */
            pwmParam_left1.output = LEFT_MOTOR_SPEED1;
            pwmParam_left1.level = kSCTIMER_HighTrue;
            pwmParam_left1.
               /* Configure first PWM with frequency 24kHZ from LEFT MOTOR SECOND SIGNAL output */
            pwmParam_left2.output = LEFT_MOTOR_DIRECTION1;
            pwmParam_left2.level = kSCTIMER_HighTrue;
            pwmParam_left2.
                  /* Configure first PWM with frequency 24kHZ from RIGHT MOTOR FIRST SIGNAL output */
            pwmParam_right1.output = RIGHT_MOTOR_SPEED2;
            pwmParam_right1.level = kSCTIMER_HighTrue;
            pwmParam_right1.
            /* Configure first PWM with frequency 24kHZ from RIGHT MOTOR SECOND SIGNAL output */
            pwmParam_right2.output = RIGHT_MOTOR_DIRECTION2;
            pwmParam_right2.level = kSCTIMER_HighTrue;
            pwmParam_right2.
    /* Schedule events in current state; State 0 */
    /* Schedule events for generating a 24KHz PWM with 10% duty cycle from first Out in the current state */
     /* Initialize SCTimer module */
        SCTIMER_Init(SCT0, &sctimerInfo);
        SCTIMER_SetupPwm(SCT0, &pwmParam_left1, kSCTIMER_CenterAlignedPwm, 24000U, sctimerClock, &event_left1);
        SCTIMER_SetupPwm(SCT0, &pwmParam_left2, kSCTIMER_CenterAlignedPwm, 24000U, sctimerClock, &event_left2);
        SCTIMER_SetupPwm(SCT0, &pwmParam_right1, kSCTIMER_CenterAlignedPwm, 24000U, sctimerClock, &event_right1);
        SCTIMER_SetupPwm(SCT0, &pwmParam_right2, kSCTIMER_CenterAlignedPwm, 24000U, sctimerClock, &event_right2);
    /* Start the timer, use counter L as we are operating counter in 32-bit mode */
    SCTIMER_StartTimer(SCT0, kSCTIMER_Counter_L);
    /* Force the counter to be placed into memory. */
    /* Enter an infinite loop, just incrementing a counter. */
    while(1) {
    if(GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_speed_PIN)==0)
    {
    while(GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_speed_PIN)==0);
    dutycycle_left=dutycycle_left+
    if(dutycycle_left>100)
    dutycycle_left=60;
    a=0;
    }
    if(GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_speed_PIN)==0)
        {
    while(GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_speed_PIN)==0);
    dutycycle_right=dutycycle_
    if(dutycycle_right>=100)
       dutycycle_right=60;
    b=0;
        }
    if(GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_dir_PIN)==0)
    {
    while(GPIO_PinRead(GPIO, MOTOR_PORT, left_motor_dir_PIN)==0);
    a=a+1;
    if (a>2)
    {
    a=0;
    }
    }
    if(GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_dir_PIN)==0)
        {
    while(GPIO_PinRead(GPIO, MOTOR_PORT, right_motor_dir_PIN)==0);
    b=b+1;
     if (b>2)
      {
      b=0;
       }}
    if(a==0){
    SCTIMER_UpdatePwmDutycycle(
    SCTIMER_UpdatePwmDutycycle(
    }
    if(a==1)
    {
    SCTIMER_UpdatePwmDutycycle(
    SCTIMER_UpdatePwmDutycycle(
    }
    if(b==0){
    SCTIMER_UpdatePwmDutycycle(
    SCTIMER_UpdatePwmDutycycle(
    }
    if(b==1){
        SCTIMER_UpdatePwmDutycycle(
        SCTIMER_UpdatePwmDutycycle(
        }
}
return 0;
}